## Slide 1
Flow Through Packed and Fluidized Beds
By
Amol Deshpande

## Slide 2
Flow through beds of solids
Motion of particles through fluids
Fluidization
Outline

## Slide 3
Objective  To study the behaviour of single phase fluid flow through a column of stationary solid particles
Resistance to the flow of fluid (leads to pressure drop)  function of total drag on solid boundaries
Calculation of this pressure drop (total drag)
  Need to take tortuous channels through the bed into consideration
Flow through beds of solids

## Slide 4
Surface to volume ratio
Sphericity
Porosity (void fraction)
Equivalent channel diameter
Superficial velocity
Average velocity
Flow through beds of solids – Important parameters

## Slide 5
Pressure drop depend on average velocity and channel diameter
Average velocity and channel diameter can be expressed in terms of measurable parameters (superficial velocity, diameter of particle, porosity)
Low Re
  Hagen-Poiseuille equation
Calculation of pressure drop

## Slide 6
Kozeny-Carman equation
  Applicable for very low Re (Rep < 1.0)
Darcy’s law
  Used to describe the flow of liquids through porous media
Burke-Plummer equation
  Applicable for high Re (Rep > 1000)
Ergun equation
Effect of void fraction on pressure drop
Calculation of pressure drop

## Slide 7
Ergun equation can be used to determine the pressure drop
Particle diameter will be replaced by surface mean diameter of the mixture.
Mixture of particles in the bed

## Slide 8
Mechanics of particle motion
  Balance of forces
    External force
    Buoyant force
    Drag force
One dimensional motion of particle through fluid
  Generalized equation
  Motion from gravitational force
  Motion in a centrifugal field
Motion of particles through fluids

## Slide 9
Terminal velocity
  Maximum attainable velocity by a particle moving through the fluid
  For gravitational settling
  In motion from centrifugal force
Drag coefficient (Fig. 7.7)
  Curve applicable under certain restrictions – like solid particle, particle is far from other particles and wall, moving with terminal velocity
Motion of particles through fluids

## Slide 10
Generalized expression for terminal velocity
Low Re (Re <1)
  Drag coefficient
  Drag force
  Terminal velocity  Stoke’s law
For high Re (1000 < Re < 200,000)
  Drag coefficient
  Drag force
  Terminal velocity  Newton’s law
Motion of spherical particles

## Slide 11
It is corresponding to the condition of fully suspended particles (as suspension behaves as dense fluid)
Fluidization

## Slide 12
Important design
parameters
  Minimum fluidization
  velocity
  Bed expansion of
  fluidization
  Pressure variation in
  bed
Fluidization

## Slide 13
Can be obtained by setting pressure drop across the bed equal to the weight of the bed per unit area of cross section
Expression for minimum fluidization velocity
  Ergun equation  quadratic equation
  Kozeny-Carman (Low Re)
    VOM is proportional to Dp2
  Burke-Plummer equation (High Re)
    VOM is proportional to Dp0.5
Minimum fluidization velocity

## Slide 14
For low Re (small particles) – Stoke’s law regime
  Both vary with Dp2 and density difference (particle and fluid) and viscosity
  Their ratio depends only on void fraction at minimum fluidization velocity and its high (Approximately 50 for spherical particles)
For high Re (coarse particles) – Newton’s law regime
  Low ratio
Terminal velocity and Minimum fluidization velocity

## Slide 15
Particulate fluidization
  Particles move farther apart and their motion becomes more vigorous as velocity is increased but average density of the bed at a given velocity is same in all sections
  E.g. Sand particles in water
Bubbling fluidization/Aggregative fluidization
  Gases pass through the solid as bubbles or voids
  E.g. solids fluidized with air
Types of fluidization

## Slide 16
Fluid catalytic cracking
  Mainly in regenerating the catalyst
Catalytic processes
  Synthesis of acrylonitrile
Solid gas reactions
Fluidized bed combustion of coal
Application of fluidization

## Slide 17
Advantages
  Solid is vigorously agitated by the fluid and there is practically no temperature gradients
  Provides high heat transfer rates to the walls of the bed
  Easy to transport solids
Disadvantages
  Uneven contacting of gas and solids
  Erosion of vessel internal parts
  Attrition of solid particles
Advantages / Disadvantages of fluidization