## Slide 1
Fundamental Concepts

## Slide 2
Fluid as a continuum
Density
Velocity field
Stress field
Viscosity
Surface tension
Description and classification of fluid motions
Outline

## Slide 3
Continuum  smooth continuous medium
Basis of classical fluid mechanics
Assumption is not valid in rarefied gas flow, etc.
Fluid as a continuum

## Slide 4
Density – Mass per unit volume
  For ideal gases
Specific volume
Specific weight
Specific Gravity (SG)
Vapor pressure
Some important properties of a fluid
Notes: Specific weight  It is the weight of a substance per unit volume (=density * gravity)
Vapor pressure  The pressure exerted by its vapor in phase equilibrium with its liquid at a given temperature.

## Slide 5
Very important property
  Time rate of change of position vector
Steady / unsteady flow
  Properties at every point in the flow field do not change with time – “Steady flow”
  Properties are varying with time in the flow field – “Unsteady flow”
Velocity Field

## Slide 6
1-D, 2-D and 3-D flows
  No of space coordinates required to specify the velocity field
Uniform flow at a given cross section
  Velocity is constant across any section normal to the flow
Uniform flow field
  Velocity is constant in the flow field (velocity is independent of space coordinates throughout the entire flow field)
Velocity Field

## Slide 7
Visual representation of a flow
Timeline
  Adjacent fluid particles in a flow field are marked at a given instant of time  Formed line is “Timeline”
Pathline
  Path or trajectory traced out by a moving fluid particle
  OR
  Line traced out by a given particle as it flows from one point to another
Timelines, Pathlines, Streaklines and Streamlines

## Slide 8
Streakline
  Locus of the positions of the fluid particles, at a particular instant, which have passed through a same fixed point
  It consists of all particles in a flow that have passed through a common point
Streamline
  A line that is everywhere tangent to the velocity field
  Streamlines are tangent to the direction of flow at every instant
  Fluid cannot cross the streamline
  Streamtube – bundle of streamlines
Timelines, Pathlines, Streaklines and Streamlines

## Slide 9
http://en.wikipedia.org/wiki/File:Streaklines_and_pathlines_animation_(low).gif
http://www-mdp.eng.cam.ac.uk/web/library/enginfo/aerothermal_dvd_only/aero/fprops/cvanalysis/node8.html
Example 2.1
Timelines, Pathlines, Streaklines and Streamlines

## Slide 10
Streamlines, streaklines and pathlines are identical for steady flows
For unsteady flows, these lines have different shapes
Timelines, Pathlines, Streaklines and Streamlines

## Slide 11
Forces on a fluid particle
  Surface forces – Pressure, friction
  Body forces – Gravity, electromagnetic
Surface forces  stresses
  Generated by motion in fluids
Concept of stress in a continuum
  Normal stress
  Shear stress
Stress field

## Slide 12
Stress components
State of a stress at a point
  Can be described completely by specifying the stresses acting on any three mutually perpendicular planes through the point.
Sign convention
Stress field

## Slide 13
Deformation of a fluid particle/element
Relation between applied shear stress and deformation rate (shear rate)
Newtonian fluids (Newton’s law of viscosity)
  Most of the common fluids (water, air, oil, etc.)
Viscosity  resistance to the flow of fluid (friction)
  Units – Pa.s, poise (g/cm.s)
Viscosity
Notes: Drag force  The force a flowing fluid exerts on a body in the flow direction

## Slide 14
Kinematic viscosity
  Ratio of absolute viscosity to density
  Units – m2/s, stoke (cm2/s)
Effect of temperature on viscosity of fluid
  Gas viscosity  increases with increase in temp.
  Liquid viscosity  decreases with increase in temp.
Example 2.2
Viscosity

## Slide 15
Non-Newtonian fluids
    Special fluids (e.g., most biological fluids, toothpaste, some paints, etc.)
  “Non-linear” fluids
  Power law (One dimensional form)
  Apparent viscosity
Viscosity

## Slide 16
Non-Newtonian fluids (Time independent)
Apparent viscosity may be time dependent
  Thixotropic fluids (viscosity decreases with time)
  Rheopectic fluids (viscosity increases with time)
Viscosity

## Slide 17
Wetted/non-wetted surface
Surface tension
  Created due to unbalanced cohesive forces experienced by molecules along the surface
  The intensity of molecular attraction per unit length along any line in the surface is called “surface tension”
  Unit of σ  N/m
Surface tension

## Slide 18
Capillary rise/ capillary depression
Surfactants – compounds reduces surface tension significantly.
Surface tension

## Slide 19
Reynolds No
Mach No
Description and classification of fluid motions

## Slide 20
The velocity for a steady incompressible flow on the xy plane is given by V=(A/x)i+(Ay/x2)j, where A=2m2/s and the coordinate are measured in meters.
Obtained the equation for streamline that passes through the point (x, y) = (1, 3).
Determine the velocity of particle at (x, y)=(1, 3)
Obtain the equation for the path line.
Calculate the time required for a fluid particle to move from x = 1m to x =2m in the flow field
Example-1

## Slide 21
Example- 2
A infinite plate is over a second plate on a layer of liquid as shown. For small gap width “d”, we assumed a linear velocity distribution in the liquid. The liquid viscocity is 0.65 centipoise and specific gravity is 0.88. Determine :
the momentum diffusivity of the liquid
The shear stress on the upper plate
The shear stress in the lower plate
The direction of each shear stress

## Slide 22
Fluid of viscosity µ1=0.1 N.s/m2 and µ2=0.15 N.s/m2 are contained between two plates (each plate is 1 m2 in area). The thickness h1=0.5mm and h2=0.3 mm respectively. Find the force F to make the upper plate move at a speed of 1m/s. what is the fluid velocity at the interface between the fluids
Example -3