## Slide 1
Flow Past Immersed Bodies
By
Dr. S. S, Baral

## Slide 2
Drag and drag coefficient
Flow through beds of solids
Motion of particles through fluids
Fluidization
Outline

## Slide 3
Solid object/body surrounded by viscous fluid
Body experiences net force and it depends on
  Relative velocity
  Body size and shape
  Fluid properties
Net force
  Drag - parallel to the direction of motion
  Lift – perpendicular to the direction of motion
Introduction

## Slide 4
Force in the direction of flow exerted by fluid on the solid.
Form drag
  Drag from the local pressure
Drag

## Slide 5
Wall drag
  Drag from the wall shear stress
There is no net drag for incompressible, inviscid flow (potential flow)
Drag

## Slide 6
Similar to skin friction coefficient (for flat surfaces)
It is used for immersed solids
Ratio of drag force per unit projected area to the product of velocity head and density
For incompressible fluid
Drag coefficient

## Slide 7
For compressible fluids
  CD = f (Re, M)
Drag coefficients of typical shapes (Fig. 7.3)
  Spheres
  Disks
  Cylinders
    Assumption – Axis of cylinder and face of disk are perpendicular to the direction of flow
Drag coefficient

## Slide 8
Stoke’s law
  For low Re, drag force for a sphere (Re < 1)
  Drag coefficient
  CD= 24/Rep
  Type of flow treated by this law  creeping flow
Drag coefficient

## Slide 9
Drag coefficient

## Slide 10
Component of fluid force perpendicular to the fluid motion (Mostly applies to airfoils)
Lift coefficient
Airfoils
  Lift and drag coefficients are function of Re and angle of attack (angle between chord and free-stream velocity vector)
Lift

## Slide 11
Objective  To study the flow behavior of single fluid phase through a column of stationary solid particles
Resistance to the flow of fluid (leads to pressure drop)  function of total drag on solid boundaries
Calculation of this pressure drop (total drag)
  Need to take tortuous channels through the bed into consideration
Flow through beds of solids

## Slide 12
Surface to Volume ratio
Sphericity
Porosity (void fraction)
Equivalent Channel Diameter
Superficial velocity
Average velocity
Flow through beds of solids – Important parameters

## Slide 13
Pressure drop depend on average velocity and channel diameter
Average velocity and channel diameter can be expressed in terms of measurable parameters (superficial velocity, diameter of particle, porosity)
Low Re
  Hagen-Poiseuille equation
Calculation of pressure drop

## Slide 14
Kozeny-Carman equation
  Applicable for very low Re (Rep <1.0)
Darcy’s law
  Used to describe the flow of liquids through porous media
Burke-Plummer equation
  Applicable for high Re (Rep>1000)
Ergun equation
Effect of void fraction on pressure drop
Calculation of pressure drop

## Slide 15
Ergun equation can be used to determine the pressure drop
Particle diameter will be replaced by surface mean diameter of the mixture.
Mixture of particles in the bed

## Slide 16
Mechanics of particle motion
  Balance of forces
    External force
    Buoyant force
    Drag force
One dimensional motion of particle through fluid
  Generalized equation
  Motion from gravitational force
  Motion in a centrifugal field
Motion of particles through fluids

## Slide 17
Terminal velocity
  Maximum attainable velocity by a particle moving through the fluid
  For gravitational settling
  In motion from centrifugal force
Drag coefficient (Fig. 7.7)
  Curve applicable under certain restrictions – like solid particle, particle is far from other particles and wall, moving with terminal velocity
Motion of particles through fluids

## Slide 18
Free settling/Hindered settling
  Drag coefficient in hindered settling is greater than in free settling
Brownian movement of the particle
  Very small particles (2 to 3 micrometer size)
  Tend to suppress the effect of gravity and settling does not occur
  Application of centrifugal force reduces the effect of brownian movement
Motion of particles through fluids

## Slide 19
Generalized expression for terminal velocity
Low Re (Re <1)
  Drag coefficient
  Drag force
  Terminal velocity  Stoke’s law
For high Re (1000 < Re < 200,000)
  Drag coefficient
  Drag force
  Terminal velocity  Newton’s law
Motion of spherical particles

## Slide 20
It is corresponding to the condition of fully suspended particles (as suspension behaves as dense fluid)
Fluidization

## Slide 21
Important design
parameters
  Minimum fluidization
  velocity
  Bed expansion of
  fluidization
  Pressure variation in
  bed
Fluidization

## Slide 22
Can be obtained by setting pressure drop across the bed equal to the weight of the bed per unit area of cross section
Expression for minimum fluidization velocity
  Ergun equation  quadratic equation
  Kozeny-Carman (Low Re)
    VOM is proportional to Dp2
  Burke-Plummer equation (High Re)
    VOM is proportional to Dp0.5
Minimum fluidization velocity

## Slide 23
For low Re (small particles) – Stoke’s law regime
  Both vary with Dp2 and density difference (particle and fluid) and viscosity
  Their ratio depends only on void fraction at minimum fluidization velocity and its high (Approximately 50 for spherical particles)
For high Re (coarse particles) – Newton’s law regime
  Low ratio
  More entrainment
Terminal velocity and Minimum fluidization velocity

## Slide 24
Particulate fluidization
  Particles move farther apart and their motion becomes more vigorous as velocity is increased but average density of the bed at a given velocity is same in all sections
  E.g. Sand particles in water
Bubbling fluidization/Aggregative fluidization
  Gases pass through the solid as bubbles or voids
  E.g. solids fluidized with air
Types of fluidization

## Slide 25
Particulate fluidization
  Relation between length of the bed and porosity (void fraction)
  For large particles
    Empirical correlation for relating superficial velocity to the porosity
  Data for glass beads is given in Fig. 7.13, 7.14, 7.15
Expansion of fluidized beds

## Slide 26
Bed expansion of particulate fluidization

## Slide 28
Fluid catalytic cracking
  Mainly in regenerating the catalyst
Catalytic processes
  Synthesis of acrylonitrile
Solid gas reactions
Fluidized bed combustion of coal
Application of fluidization

## Slide 29
Advantages
  Solid is vigorously agitated by the fluid and there is practically no temperature gradients
  Provides high heat transfer rates to the walls of the bed
  Easy to transport solids
Disadvantages
  Uneven contacting of gas and solids
  Erosion of vessel internal parts
  Attrition of solid particles
Advantages / Disadvantages of fluidization